MODEL FLOODPLAIN MANAGEMENT ORDINANCE

39

The following model ordinance pertains only to those communities participating in the Emergency Program

Phase of the National Flood Insurance Program without identified flood-prone areas. It has been designed

to meet minimum Federal requirements as published in Title 44 of the Code of Federal Regulations.

Not all sections in this model ordinance may be applicable to a community that wishes to adopt a floodplain

management ordinance. Before adoption, this model ordinance should be thoroughly studied by community

officials, planning commissions, and the community's attorney, as to its adequacy and suitability to the

community's needs. This will ensure that the community's specific floodplain management issues are

governed in a reasonable manner without inflicting unnecessary hardships on people living in flood-prone

areas.

This model does not prohibit development in flood-prone areas. It does set forth minimum performance

standards for new construction or substantially improved structures. Communities may apply stricter

regulations than the minimum Federal requirements. For assistance in tailoring this ordinance to meet your

community's specific needs, a Community Mitigation Programs Specialist may be contacted at the

following address:

Federal Emergency Management Agency

Mitigation Division

2323 Grand Boulevard, Suite 900

Kansas City, Missouri 64108-2670

Phone: (816) 283-7002

FLOODPLAIN MANAGEMENT ORDINANCE

39

ARTICLE 1: STATUTORY AUTHORIZATION, FINDINGS OF FACT, AND PURPOSES

SECTION A. STATUTORY AUTHORIZATION

The Legislature of the State of Iowa has in Chapter 364, Code of Iowa, as amended, delegated the power

to cities to exercise any power and perform any function it deems appropriate to protect and preserve the

rights, privileges and property of the City or of its residents, and to preserve and improve the peace, safety,

health, welfare, comfort and convenience of its residents. Therefore, the Union County Board of

Supervisors Union County, Iowa ordains as follows:

SECTION B. FINDINGS OF FACT

1. Flood Losses Resulting from Periodic Inundation

The flood-prone areas of Union County, Iowa are subject to inundation which results in loss of life

and property, health and safety hazards, disruption of commerce and governmental services,

extraordinary public expenditures for flood protection and relief, and impairment of the tax base;

all of which adversely affect the public health, safety and general welfare.

2. General Causes of the Flood Losses

These flood losses are caused by (1) the cumulative effect of development in any flood-prone area

causing increases in flood heights and velocities; and (2) the occupancy of flood-prone areas by

uses vulnerable to floods, hazardous to others, inadequately elevated, or otherwise unprotected from

flood damages.

SECTION C. STATEMENT OF PURPOSE

It is the purpose of this ordinance to promote the public health, safety, and general welfare; to minimize

those losses described in Article 1, Section B (1); to establish or maintain the community's eligibility for

participation in the National Flood Insurance Program (NFIP) as defined in 44 Code of Federal Regulations

(CFR) 59.22(a)(3); and to meet the requirements of 44 CFR 60.3(a) by applying the

provisions of this ordinance to:

1. restrict or prohibit uses that are dangerous to health, safety, or property in times of flooding or

cause undue increases in flood heights or velocities;

2. require uses vulnerable to floods, including public facilities that serve such uses, be provided

with flood protection at the time of initial construction; and

3. protect individuals from buying lands that are unsuited for the intended development purposes

due to the flood hazard.

ARTICLE 2: GENERAL PROVISIONS

SECTION A. LANDS TO WHICH ORDINANCE APPLIES

This ordinance shall apply to all lands within the jurisdiction of the Union County, Iowa that have been

identified by the community as having the presence of flood-prone areas. In all areas covered by this

ordinance, no development shall be permitted except through the issuance of a floodplain development

permit, granted by the Union County, Iowa or its duly designated representative under such safeguards and

restrictions as the Union County, Iowa or the designated representative may reasonably impose for the

promotion and maintenance of the general welfare, health of the inhabitants of the community, and as

specifically noted in Article 4.

SECTION B. FLOODPLAIN ADMINISTRATOR

Jo Anne Duckworth, Director of the Union County Emergency Management Agency, is hereby designated

as the Floodplain Administrator under this ordinance.

SECTION C COMPLIANCE

No development located within the flood-prone areas of this community shall be located, extended,

converted, or structurally altered without full compliance with the terms of this ordinance and other

applicable regulations

SECTION D. ABROGATION AND GREATER RESTRICTIONS

It is not intended by this ordinance to repeal, abrogate, or impair any existing easements, covenants, or deed

restrictions. However, where this ordinance imposes greater restrictions, the provisions of this ordinance

shall prevail. All other ordinances inconsistent with this ordinance are hereby repealed to the extent of the

inconsistency only.

SECTION E. INTERPRETATION

In their interpretation and application, the provisions of this ordinance shall be held to be minimum

requirements, shall be liberally construed in favor of the governing body, and shall not be deemed a

limitation or repeal of any other powers granted by the Code of Iowa.

SECTION F. WARNING AND DISCLAIMER OF LIABILITY

The degree of flood protection required by this ordinance is considered reasonable for regulatory purposes

and is based on the community's knowledge of past flooding. Larger floods may occur on rare occasions

or the flood heights may be increased by man-made or natural causes, such as ice jams and bridge openings

restricted by debris. This ordinance does not imply that areas outside the floodplain or land uses permitted

within such areas will be free from flooding or flood damage. This ordinance shall not create a liability on

the part of Union County, Iowa any officer or employee thereof, for any flood damages that may result from

reliance on this ordinance or any administrative decision lawfully made thereunder.

SECTION G. SEVERABILITY

If any section, clause, provision, or portion of this ordinance is adjudged unconstitutional or invalid by a

court of appropriate jurisdiction, the remainder of this ordinance shall not be affected thereby.

ARTICLE 3: ADMINISTRATION

SECTION A. FLOODPLAIN DEVELOPMENT PERMIT (REQUIRED)

A floodplain development permit shall be required for all proposed construction or other development,

including the placement of factory-built homes, so that it may be determined whether such construction or

other development is proposed within flood-prone areas. No person, firm, corporation, or unit of

government shall initiate any development or substantial-improvement or cause the same to be done

without first obtaining a separate floodplain development permit for each structure or other development.

SECTION B DESIGNATION OF FLOODPLAIN ADMINISTRATOR

Jo Anne Duckworth, Director of the Union County Emergency Management Agency is hereby appointed

to administer and implement the provisions of this ordinance.

SECTION C. DUTIES AND RESPONSIBILITIES OF FLOODPLAIN ADMINISTRATOR

Duties of the floodplain administrator shall include, but not be limited to:

1. review of all applications for floodplain development permits to assure that sites are reasonably safe

from flooding and that the floodplain development permit requirements of this ordinance have been

satisfied;

2. review of all applications for floodplain development permits for proposed development to assure

that all necessary permits have been obtained from Federal, State, or local governmental agencies

from which prior approval is required by Federal, State, or local law;

3. review all subdivision proposals and other proposed new development, including manufactured

home parks or subdivisions, to determine whether such proposals will be reasonably safe from

flooding;

4. issue floodplain development permits for all approved applications;

5. notify adjacent communities and Iowa Department of Natural Resources (DNR) prior to any

alteration or relocation of a watercourse, and submit evidence of such notification to the Federal

Emergency Management Agency (FEMA); and

6. assure that maintenance is provided within the altered or relocated portion of any watercourse so

that the flood-carrying capacity is not diminished

SECTION D. APPLICATION FOR FLOODPLAIN DEVELOPMENT PERMIT

To obtain a floodplain development permit, the applicant shall first file an application in writing on a form

furnished for that purpose. Every floodplain development permit application shall:

1. describe the land on which the proposed work is to be done by lot, block and tract, house and

street address, or similar description that will readily identify and specifically locate the proposed

building or work,

2. identify and describe the work to be covered by the floodplain development permit;

3. indicate the use or occupancy for which the proposed work is intended;

4. indicate the assessed value of the structure and the fair market value of the improvement,

5. give such other information as reasonably may be required by the floodplain administrator;

6. be accompanied by plans and specifications for proposed construction; and

7. be signed by the permittee or his authorized agent who may be required to submit evidence to

indicate such authority.

ARTICLE 4: PROVISIONS FOR FLOOD HAZARD REDUCTION

SECTION A. GENERAL STANDARDS

1. No permit for floodplain development shall be granted for new construction, substantial

improvements, and other improvements, including the placement of factory-built homes, within

any flood-prone area unless the conditions of this section are satisfied

2. All new construction, subdivision proposals, substantial-improvements, prefabricated buildings,

placement of factory-built homes, and other developments within flood-prone areas shall require:

a. design or adequate anchorage to prevent flotation, collapse, or lateral movement of the

structure resulting from hydrodynamic and hydrostatic loads, including the effects of

buoyancy;

b. construction with materials resistant to flood damage;

c. utilization of methods and practices that minimize flood damages;

d. all electrical, heating, ventilation, plumbing, air-conditioning equipment, and other service

facilities be designed and/or located so as to prevent water from entering or accumulating

within the components during conditions of flooding;

e. new or replacement water supply systems and/or sanitary sewage systems be designed to

minimize or eliminate infiltration of flood waters into the systems and discharges from the

systems into flood waters, and on-site waste disposal systems be located so as to avoid

impairment or contamination; and

Wastewater treatment facilities and water supply treatment facilities (other than on-site

systems) shall be provided with a level of protection equal to or greater than one (1) foot

above the 100-year flood level.

f. subdivision proposals and other proposed new development, including manufactured home

parks or subdivisions, located within flood-prone areas are required to assure that:

(1) all such proposals are consistent with the need to minimize flood damage;

(2) all public utilities and facilities, such as sewer, gas, electrical, and water systems

are located and constructed to minimize or eliminate flood damage; and

(3) adequate drainage is provided so as to reduce exposure to flood hazards.

3. Storage, material, and equipment

a. The storage or processing of materials within flood-prone areas that are in time of

flooding buoyant, flammable, explosive, or could be injurious to human, animal, or plant

life is prohibited unless elevated a minimum of one (1) foot above the 100-year level.

b. Storage of other material or equipment may be allowed if such material or equipment is

elevated a minimum of one (1) foot above the 100-year flood level and not subject to major

damage by floods, if firmly anchored to prevent flotation, or if readily removable from the

area within the time available after a flood warning.

4. Agricultural Structures

Structures used solely for agricultural purposes in connection with the production, harvesting,

storage, drying, or raising of agricultural commodities, including the raising of livestock, may be

constructed at-grade and wet-floodproofed provided there is no human habitation or occupancy of

the structure; the structure is of single-wall design; there is no permanent retail, wholesale, or

manufacturing use included in the structure; a variance has been granted from the floodplain

management requirements of this ordinance; and a floodplain development permit has been issued.

5. Accessory Structures

Structures used solely for parking and limited storage purposes, not attached to any other structure

on the site, of limited investment value, and not larger than 400 square feet, may be constructed

at-grade and wet-floodproofed provided there is no human habitation or occupancy of the structure;

the structure is of single-wall design; a variance has been granted from the standard floodplain

management requirements of this ordinance; and a floodplain development permit has been issued.

6. Hazardous Materials

All hazardous material storage and handling sites shall be located out of the floodplain.

7. Nonconforming Use

A structure, or the use of a structure or premises that was lawful before the passage or amendment

of the ordinance, but which is not in conformity with the provisions of this ordinance, may be

continued subject to the following conditions:

a. If such structure, use, or utility service is discontinued for twelve consecutive months, any

future use of the building shall conform to this ordinance.

b. If any nonconforming use or structure is destroyed by any means, including flood, it shall

not be reconstructed if the cost is more than 50 percent of the pre-damaged market value

of the structure. This limitation does not include the cost of any alteration to comply with

existing state or local health, sanitary, building, safety codes, regulations or the cost of any

alteration of a structure listed on the National Register of Historic Places, the State

Inventory of Historic Places, or local inventory of historic places upon determination.

8. Critical Facilities

a. All new or substantially improved critical nonresidential facilities including, but not

limited, to governmental buildings, police stations, fire stations, hospitals, orphanages,

penal institutions, communication centers, water and sewer pumping stations, water and

sewer treatment facilities, transportation maintenance facilities, places of public assembly,

emergency aviation facilities, and schools shall be elevated above the 500-year flood level

or together with attendant utility and sanitary facilities, be floodproofed so that below the

500-year flood level the structure is water tight with walls substantially impermeable to the

passage of water and with structural components having the capability of resisting

hydrostatic and hydrodynamic loads and the effects of buoyancy. A registered professional

engineer or architect shall certify that the standards of this subsection are satisfied. Such

certification shall be provided to the Floodplain Administrator as set forth in the National

Flood Insurance Program (NFIP) regulations.

b. All critical facilities shall have access routes that are above the elevation of the 500-year

flood.

c. If any nonconforming use or structure is destroyed by any means, including flood, it shall

not be reconstructed if the cost is more than 50 percent of the pre-damaged market value

of the structure. This limitation does not include the cost of any alteration to comply with

existing state or local health, sanitary, building, safety codes, regulations or the cost of any

alteration of a structure listed on the National Register of Historic Places, the State

Inventory of Historic Places, or local inventory of historic places upon determination.

SECTION B. FACTORY-BUILT HOMES

1. All factory-built homes to be placed within flood-prone areas shall be required to be installed

using methods and practices that minimize flood damage. For the purposes of this requirement,

factory-built homes must be anchored to resist flotation, collapse, or lateral movement. Methods

of anchoring may include, but are not limited to, use of over-the-top or frame ties to ground

anchors.

SECTION C. RECREATIONAL VEHICLES

1. Require that recreational vehicles placed on sites within flood-prone areas:

a. be on the site for fewer than 180 consecutive days, or

b. be fully licensed and ready for highway use*, or

c. meet the permitting and anchoring requirements for factory-built homes of this ordinance.

*A recreational vehicle is ready for highway use if it is on its wheels or jacking system, is attached to the

site only by quick-disconnect type utilities and security devices, and has no permanently attached additions.

ARTICLE 5: FLOODPLAIN MANAGEMENT VARIANCE PROCEDURES

SECTION A. ESTABLISHMENT OF APPEAL BOARD

The Union County Board of Supervisors shall hear and decide appeals and requests for variances from the

floodplain management requirements of this ordinance.

SECTION B. RESPONSIBILITY OF APPEAL BOARD

Where an application for a floodplain development permit or request for a variance from the floodplain

management regulations is denied by the floodplain administrator, the applicant may apply for such

floodplain development permit or variance directly to the Appeal Board, as defined

in Article 5, Section A.

The Union County Board of Supervisors shall hear and decide appeals when it is alleged that there is an

error in any requirement, decision, or determination made by the floodplain administrator in the

enforcement or administration of this ordinance.

SECTION C. FURTHER APPEALS

Any person aggrieved by the decision of the Union County Board of Supervisors or any taxpayer may

appeal such decision to the District Court as provided by statute.

SECTION D. FLOODPLAIN MANAGEMENT VARIANCE CRITERIA

In passing upon such applications for variances, the Union County Board of Supervisors shall consider all

technical data and evaluations, all relevant factors, standards specified in other sections of this ordinance,

and the following criteria

1. the danger to life and property due to flood damage;

2. the danger that materials may be swept onto other lands to the injury of others;

3. the susceptibility of the proposed facility and its contents to flood damage and the effect of such

damage on the individual owner,

4. the importance of the services provided by the proposed facility to the community;

5. the necessity to the facility of a waterfront location, where applicable;

6. the availability of alternative locations, not subject to flood damage, for the proposed use;

7. the compatibility of the proposed use with existing and anticipated development;

8. the relationship of the proposed use to the comprehensive plan and floodplain management

program for that area;

9. the safety of access to the property in times of flood for ordinary and emergency vehicles;

10. the expected heights, velocity, duration, rate of rise and sediment transport of the flood waters,

if applicable, expected at the site; and,

11. the costs of providing governmental services during and after flood conditions including

maintenance and repair of public utilities and facilities such as sewer, gas, electrical, and water

systems; streets; and bridges.

SECTION E. CONDITIONS FOR APPROVING FLOODPLAIN MANAGEMENT VARIANCES

1. Generally, variances may be issued for new construction and substantial-improvements to be

erected on a lot of one-half acre or less in size contiguous to and surrounded by lots with existing

structures constructed below highest adjacent grade, providing items 2 through 5 below have been

fully considered. As the lot size increases beyond the one-half acre, the technical justification

required for issuing the variance increases.

2. Variances may be issued for the reconstruction, rehabilitation, or restoration of structures listed on

the National Register of Historic Places, the State Inventory of Historic Places, or local inventory

of historic places upon determination provided the proposed activity will not preclude the structure's

continued historic designation,

3. Variances shall only be issued upon a determination that the variance is the minimum necessary,

considering the flood hazard, to afford relief.

4. Variances shall only be issued upon (a) a showing of good and sufficient cause, (b) a determination

that failure to grant the variance would result in exceptional hardship to the applicant, and (c) a

determination that the granting of a variance will not result in increased flood heights, additional

threats to public safety, extraordinary public expense, create nuisances, cause fraud on or

victimization of the public, or conflict with existing local laws or ordinances.

5. A community shall notify the applicant in writing over the signature of a community official

that the issuance of a variance to construct a structure below highest adjacent grade will result in

increased premium rates for flood insurance up to amounts as high as $25.00 for $100.00 of

insurance coverage and (2) such construction below highest adjacent grade increases risks to life

and property. Such notification shall be maintained with the record of all variance actions as

required by this ordinance.

SECTION F. CONDITIONS FOR APPROVING VARIANCES FOR AGRICULTURAL STRUCTURES

Any variance granted for an agricultural structure shall be decided individually based on a case by case

analysis of the building's unique circumstances. Variances granted shall meet the following conditions as

well as those criteria and conditions set forth in Article 5, Sections D and E of this ordinance.

In order to minimize flood damages during the 100-year flood and the threat to public health and safety,

the following conditions shall be included for any variance issued for agricultural structures that are

constructed at-grade and wet-floodproofed.

1. All agricultural structures considered for a variance from the floodplain management

regulations of this ordinance shall demonstrate that the varied structure is located in wide,

expansive floodplain areas and no other alternate location outside of the floodplain exists for the

agricultural structure. Residential structures, such as farm houses, cannot be considered

agricultural structures.

2. Use of the varied structures must be limited to agricultural purposes in flood-prone areas only.

3. For any new or substantially damaged agricultural structures, the exterior and interior building

components and elements (i.e., foundation, wall framing, exterior and interior finishes, flooring,

etc.) below highest adjacent grade, must be built with flood-resistant materials in accordance with

Article 4, Section A (2)(b) of this ordinance.

4. The agricultural structures must be adequately anchored to prevent flotation, collapse, or lateral

movement of the structures in accordance with Article 4, Section A (2)(a) of this ordinance. All of

the building's structural components must be capable of resisting specific flood-related forces

including hydrostatic, buoyancy, and hydrodynamic and debris impact forces.

5. Any mechanical, electrical, or other utility equipment must be located above highest adjacent grade

or floodproofed so that they are contained within a watertight, floodproofed enclosure that is

capable of resisting damage during flood conditions in accordance with Article 4, Section A (2)(d)

of this ordinance.

6. The agricultural structures must meet all National Flood Insurance Program (NFIP) opening

requirements. The NFIP requires that enclosure or foundation walls, subject to the 100-year flood,

contain openings that will permit the automatic entry and exit of floodwaters in accordance with

the NFIP regulations.

7. Major equipment, machinery, or other contents must be protected from any flood damage.

8. No disaster relief assistance under any program administered by any Federal agency shall be paid

for any repair or restoration costs of the agricultural structures.

9. A community shall notify the applicant in writing over the signature of a community official that

the issuance of a variance to construct a structure below highest adjacent grade will result in

increased premium rates for flood insurance up to amounts as high as $25.00 for $100.00 of

insurance coverage and (2) such construction below highest adjacent grade increases risks to life

and property. Such notification shall be maintained with the record of all variance actions as

required by this ordinance.

10. Wet-floodproofing construction techniques must be reviewed and approved by the community and

a registered professional engineer or architect prior to the issuance of any floodplain development

permit for construction.

SECTION G. CONDITIONS FOR APPROVING VARIANCES FOR ACCESSORY STRUCTURES

Any variance granted for an accessory structure shall be decided individually based on a case by case

analysis of the building's unique circumstances. Variances granted shall meet the following conditions as

well as those criteria and conditions set forth in Article 5, Sections D and E of this ordinance.

In order to minimize flood damages during the 100-year flood and the threat to public health and safety,

the following conditions shall be included for any variance issued for accessory structures that are

constructed at-grade and wet-floodproofed.

1. Use of the accessory structures must be solely for parking and limited storage purposes in flood

prone areas only.

2. For any new or substantially damaged accessory structures, the exterior and interior building

components and elements (i.e., foundation, wall framing, exterior and interior finishes, flooring,

etc.) below highest adjacent grade, must be built with flood-resistant materials in accordance with

Article 4, Section A (2)(b) of this ordinance.

3. The accessory structures must be adequately anchored to prevent flotation, collapse, or lateral

movement of the structure in accordance with Article 4, Section A (2)(a) of this ordinance. All of

the building's structural components must be capable of resisting specific flood-related forces

including hydrostatic, buoyancy, and hydrodynamic and debris impact forces.

4. Any mechanical, electrical, or other utility equipment must be located above highest adjacent

grade or floodproofed so that they are contained within a watertight, floodproofed enclosure that

is capable of resisting damage during flood conditions in accordance with Article 4, Section A

(2)(d) of this ordinance.

5. The accessory structures must meet all National Flood Insurance Program (NF1P) opening

requirements. The NFIP requires that enclosure or foundation walls, subject to the 100-year flood,

contain openings that will permit the automatic entry and exit of floodwaters in accordance with

the NFIP regulations.

6. Equipment, machinery, or other contents must be protected from any flood damage.

7. No disaster relief assistance under any program administered by any Federal agency shall be

paid for any repair or restoration costs of the accessory structures.

8. A community shall notify the applicant in writing over the signature of a community official that

(1) the issuance of a variance to construct a structure below highest adjacent grade will result in

increased premium rates for flood insurance up to amounts as high as $25.00 for $100.00 of

insurance coverage and (2) such construction below highest adjacent grade increases risks to life

and property. Such notification shall be maintained with the record of all variance actions as

required by this ordinance.

9. Wet-floodproofing construction techniques must be reviewed and approved by the community and

registered professional engineer or architect prior to the issuance of any floodplain development

permit for construction.

ARTICLE 6: PENALTIES FOR VIOLATION

Violation of the provisions of this ordinance or failure to comply with any of its requirements (including

violations of conditions and safeguards established in connection with granting of variances) shall

constitute a simple misdemeanor. Any person who violates this ordinance or fails to comply with any of

its requirements shall, upon conviction thereof, be fined not more than $625.00, and in addition, shall pay

all costs and expenses involved in the case. Each day such violation continues shall be considered a

separate offense. Nothing herein contained shall prevent Union County or other appropriate authority from

taking such other lawful action as is necessary to prevent or remedy any violation.

ARTICLE 7: AMENDMENTS

The regulations, restrictions, and boundaries set forth in this ordinance may from time to time be amended,

supplemented, changed, or appealed to reflect any and all changes in the National Flood Disaster Protection

Act of 1973, provided, however, that no such action may be taken until after a public hearing in relation

thereto, at which parties of interest and citizens shall have an opportunity to be heard. Notice of the time

and place of such hearing shall be published in a newspaper of general circulation in Union County, Iowa.

At least 20 days shall elapse between the date of this publication and the public hearing. A copy of such

amendments will be provided to the Region VII office of the Federal Emergency Management Agency

(FEMA). The regulations of this ordinance are in compliance with the National Flood Insurance Program

(NFIP) regulations.

ARTICLE 8: DEFINITIONS

Unless specifically defined below, words or phrases used in this ordinance shall be interpreted so as to give

them the same meaning they have in common usage and to give this ordinance its most reasonable

application.

"100-year Flood" see "base flood."

"Accessory Structure" means the same as "appurtenant structure. "

"Actuarial Rates" see "risk premium rates. "

"Administrator" means the Federal Insurance Administrator.

"Agency" means the Federal Emergency Management Agency (FEMA).

"Agricultural Commodities" means agricultural products and livestock.

"Agricultural Structure" means any structure used exclusively in connection with the production,

harvesting, storage, drying, or raising of agricultural commodities.

"Appeal" means a request for review of the Floodplain Administrator's interpretation of any provision of

this ordinance or a request for a variance

"Appurtenant Structure" means a structure that is on the same parcel of property as the principle structure

to be insured and the use of which is incidental to the use of the principal structure.

"Base Flood" means the flood having a one percent chance of being equaled or exceeded in any given year.

"Basement" means any area of the building having its floor subgrade (below ground level) on all sides.

"Building" see "structure."

"Chief Executive Officer" or "Chief Elected Official" means the official of the community who is charged

with the authority to implement and administer laws, ordinances, and regulations for that community.

"Community" means any State or area or political subdivision thereof, which has authority to adopt and

enforce floodplain management regulations for the areas within its jurisdiction.

"Development" means any man-made change to improved or unimproved real estate, including but not

limited to buildings or other structures, levees, levee systems, mining, dredging, filling, grading, paving,

excavation or drilling operations, or storage of equipment or materials.

"Eligible Community" or "Participating Community" means a community for which the Administrator has

authorized the sale of flood insurance under the National Flood Insurance Program (NFIP).

"Existing Manufactured Home Park or Subdivision" means a manufactured home park or subdivision for

which the construction of facilities for servicing the lots on which the factory-built homes are to be affixed

(including, at a minimum, the installation of utilities, the construction of streets, and either final site grading

or the pouring of concrete pads) is completed before the effective date of the floodplain management

regulations adopted by a community.

"Expansion to an Existing Manufactured Home Park or Subdivision" means the preparation of additional

sites by the construction of facilities for servicing the lots on which the factory-built homes are to be affixed

(including the installation of utilities, the construction of streets, and either final site grading or the pouring

of concrete pads).

"Flood" or "Flooding" means a general and temporary condition of partial or complete inundation of

normally dry land areas from (1) the overflow of inland and/or (2) the unusual and rapid accumulation or

runoff of surface waters from any source

"Floodplain" or "Flood-prone Area" means any land area susceptible to being inundated by water from any

source (see "flooding').

"Floodplain Management" means the operation of an overall program of corrective and preventive

measures for reducing flood damage, including but not limited to emergency preparedness plans, flood

control works, and fl oodplain management regulations.

"Floodplain Management Regulations" means zoning ordinances, subdivision regulations, building codes,

health regulations, special purpose ordinances (such as floodplain and grading ordinances) and other

applications of police power. The term describes such state or local regulations, in any combination thereof,

that provide standards for the purpose of flood damage prevention and reduction.

"Floodproofing" means any combination of structural and nonstructural additions, changes, or adjustments

to structures that reduce or eliminate flood damage to real estate or improved real property, water and

sanitary facilities, or structures and their contents.

"Functionally Dependent Use" means a use that cannot perform its intended purpose unless it is located or

carried out in close proximity to water. This term includes only docking facilities and facilities that are

necessary for the loading and unloading of cargo or passengers, but does not include long-term storage or

related manufacturing facilities.

"Historic Structure" means any structure that is (a) listed individually in the National Register of Historic

Places (a listing maintained by the Department of Interior) or preliminarily determined by the

Secretary of the Interior as meeting the requirements for individual listing on the National Register; (b)

certified or preliminarily determined by the Secretary of the Interior as contributing to the historical

significance of a registered historic district or a district preliminarily determined by the Secretary to qualify

as a registered historic district; (c) individually listed on a state inventory of historic places in states with

historic preservation programs which have been approved by the Secretary of the Interior; or (d)

individually listed on a local inventory of historic places in communities with historic preservation

programs that have been certified either (1) by an approved state program as determined by the Secretary

of the Interior or (2) directly by the Secretary of the Interior in states without approved

programs

"Lowest Floor" means the lowest floor of the lowest enclosed area (including basement). An unfinished

or flood-resistant enclosure, usable solely for parking of vehicles, building access, or storage, in an area

other than a basement area, is not considered a building's lowest floor, provided that such enclosure is not

built so as to render the structure in violation of the applicable floodproofing design requirements of this

ordinance.

"Manufactured Home" means a structure, transportable in one or more sections, that is built on a permanent

chassis and is designed for use with or without a permanent foundation when attached to the required

utilities. The term "manufactured home" does not include a "recreational vehicle. "

"Manufactured Home Park or Subdivision" means a parcel (or contiguous parcels) of land divided into two

or more manufactured home lots for rent or sale

"Market Value" or "Fair Market Value" means an estimate of what is fair, economic, just and equitable

value under normal local market conditions.

"New Manufactured Home Park or Subdivision" means a manufactured home park or subdivision for which

the construction of facilities for servicing the lot on which the factory-built homes are to be affixed

(including at a minimum, the installation of utilities, the construction of streets, and either final site grading

or the pouring of concrete pads) is completed on or after the effective date of floodplain management

regulations adopted by the community.

"(NFIP)" means the National Flood Insurance Program (NF1P).

"Participating Community" also known as an "eligible community, " means a community in which the

Administrator has authorized the sale of flood insurance.

"Person" includes any individual or group of individuals, corporation, partnership, association, or any other

entity, including Federal, State, and local governments and agencies.

"Principally Above Ground" means that at least 51 percent of the actual cash value of the structure, less

land value, is above ground.

"Recreational Vehicle" means a vehicle which is (a) built on a single chassis, (b) 400 square feet or less

when measured at the largest horizontal projections; (c) designed to be self-propelled or

permanently towable by a light- duty truck; and (d) designed primarily not for use as a permanent dwelling

but as temporary living quarters for recreational, camping, travel, or seasonal use.

"Remedy A Violation" means to bring the structure or other development into compliance with Federal,

State, or local floodplain management regulations, or, if this is not possible, to reduce the impacts of its

noncompliance,

"Risk Premium Rates" means those rates established by the Administrator pursuant to individual

community studies and investigations which are undertaken to provide flood insurance in accordance with

Section 1307 of the National Flood Disaster Protection Act of 1973 and the accepted actuarial principles.

"Risk premium rates" include provisions for operating costs and allowances.

"Start of Construction" includes substantial-improvements, and means the date the building permit was

issued, provided the actual start of construction, repair, reconstruction, rehabilitation, addition placement,

or other improvements were within 180 days of the permit date. The actual start means either the first

placement of permanent construction of a structure on a site, such as the pouring of slabs or footings, the

installation of piles, the construction of columns, any work beyond the stage of excavation, or the

placement of a manufactured home on a foundation. Permanent construction does not include land

preparation, such as clearing, grading and filling, the installation of streets and/or walkways, excavation

for a basement, footings, piers, foundations, the erection of temporary forms, nor installation on the

property of accessory buildings, such as garages or sheds not occupied as dwelling units or not part of the

main structure. For a substantial-improvement, the actual start of construction means the first alteration of

any wall, ceiling, floor, or other structural part of a building, whether or not that alteration affects the

external dimensions of the building.

"State Coordinating Agency" means that agency of the state government, or other office designated by the

governor of the state or by state statute at the request of the Administrator to assist in the implementation

of the National Flood Insurance Program (NFIP) in that state.

"Structure" means, for floodplain management purposes, a walled and roofed building, including a gas or

liquid storage tank, that is principally above ground, as well as a manufactured home. "Structure" for

insurance purposes, means a walled and roofed building, other than a gas or liquid storage tank, that is

principally above ground and affixed to a permanent site, as well as a manufactured home on a permanent

foundation. For the latter purpose, the term includes a building while in the course of construction,

alteration or repair, but does not include building materials or supplies intended for use in such

construction, alteration or repair, unless such materials or supplies are within an enclosed building on the

premises

"Substantial-Damage" means damage of any origin sustained by a structure whereby the cost of restoring

the structure to pre-damaged condition would equal or exceed 50 percent of the market value of the

structure before the damage occurred.

"Substantial-Improvement" means any reconstruction, rehabilitation, addition, or other improvement of a

structure, the cost of which equals or exceeds 50 percent of the market value of the structure before

"start of construction" of the improvement. This term includes structures which have incurred

"substantial-damage," regardless of the actual repair work performed. The term does not, however, include

either (1) any project for improvement of a structure to correct existing violations of state or local health,

sanitary, or safety code specifications that have been identified by the local code enforcement official and

which are the minimum necessary to assure safe living conditions, or (2) any alteration of a "historic

structure, " provided that the alteration will not preclude the structure's continued designation as a "historic

structure."

"Temporary Structure" means a structure permitted in a district for a period not to exceed 180 days and is

required to be removed upon the expiration of the permit period. Temporary structures may include

recreational vehicles, temporary construction offices, or temporary business facilities used until permanent

facilities can be constructed, but at no time shall it include factory-built homes used as residences

"Variance" means a grant of relief by the community from the terms of a floodplain management

regulation. Flood insurance requirements remain in place for any varied use or structure and cannot be

varied by the community,

"Violation" means the failure of a structure or other development to be fully compliant with the

community's floodplain management regulations. A structure or other development without the elevation

certificate, other certifications, or other evidence of compliance required by this ordinance is presumed to

be in violation until such time as that documentation is provided.

ARTICLE 9: CERTIFICATE OF ADOPTION

This Floodplain Management Ordinance for the community of Union County, Iowa, is ADOPTED AND

APPROVED by the Union County Board of Supervisors.

This 1st day of May, 2017.

_________________________________________________

Dennis Brown, Chair

Union County Board of Supervisors

ATTEST:

___________________________________________

Sandy Hysell, Union County Auditor

Secretary to the Board

SAMPLE FORM

1. Floodplain Development Permit/Application

FLOOD PLAIN DEVELOPMENT APPLICATION/PERMIT

Application #_____________________________ Date ______________________

TO THE ADMINISTRATOR: The undersigned hereby makes application for a Permit to develop in a flood

plain. The work to be performed, including flood protection works, is as described below and in

attachments hereto. The undersigned agrees that all such work shall be done in accordance with the

requirements of the Union County, Iowa Flood Plain Management Ordinance and with all other applicable

county/city ordinances and the laws and regulations of the State of Iowa.

______________________________ ___________ __________________________ ___________

(Owner or Agent) (Date) (Builder) (Date)

______________________________________ ___________________________________

(Address) Address)

Telephone # ____________________________ Telephone # _____________________

1. Location: _______ 1/4 _________ 1/4, Section_______, Township ______, Range _______

Street Address: _______________________________________________________

2. Type of Development

Filling_____ Grading_____ Excavation_____ Routine Maintenance_____

Minor Improvement_____ Substantial Improvement_____ New Construction_____

3. Description of Development: _____________________________________________________

_____________________________________________________________________________

4. Premises: Size of site: ___ft. x ___ft. Area of site: ____________ sq. ft.

Estimated cost: $_____________

Principal Use (Accessory, Uses, Storage, Parking, etc: _________________________________

_____________________________________________________________________________

5. Addition or modification to non-conforming use? Yes ___ No ___

Assessed value of structure: $________________

6. Elevation of the 100-year (base) flood (identify source): ________________________________

_____________________________________________________________________________

7. Elevation of the proposed development sit (natural ground):__________________ MSL/NAVD

8. Required elevation/floodproofing elevation for lowest flor: __________________ MSL/NAVD

9. Proposed elevation/floodproofing level for lowest floor (including basement): ______________

_______________________ MSL/NAVD

10. Other flood plain information (identify and describe source) ____________________________

_____________________________________________________________________________

THIS PERMIT IS ISSUED WITH THE CONDITION THAT THE LOWEST FLOOR (INCLUDING

BASEMENT) OF ANY NEW OR SUBSTANTIALLY IMPROVED RESIDENTIAL BUILDING WILL

BE ELEVATED AT LEAST 1.0 FOOT. ABOVE THE 100 YR. (BASE) FLOOD ELEVATION. IF THE

PROPOSED DEVELOPMENT IS A NON-RESIDENTIAL BUILDING, THIS PERMIT IS ISSUED

WITH THE CONDITION THAT THE LOWEST FLOOR (INCLUDING BASEMENT) OF A NEW OR

SUBSTANTIALLY IMPROVED NON-RESIDENTIAL BUILDING WILL BE ELEVATED OR FLOOD

PROOFED TO AT LEAST 1.0 FOOT ABOVE THE 100 YR. (BASE) FLOOD ELEVATION.

11. Other permits required?

Iowa Department of Natural Resources: ____ Yes ____ No

If yes, permit #:____________________________

Date Received: ____________________________

Corps of Engineers: ____ Yes ____ No

If yes, permit #:____________________________

Date Received: ____________________________

Other: ______________________________________________________________________

All provisions of the County of Union County, Iowa, Flood Plain Management Ordinance (Ordinance

Number ) shall be complied with.

THIS PERMIT IS ISSUED WITH THE CONDITION THAT THE DEVELOPER/OWNER WILL

PROVIDE CERTIFICATION BY A REGISTERED ENGINEER, ARCHITECT, OR LAND SURVEYOR

OF THE "AS-BUILT" LOWEST FLOOR (INCLUDING BASEMENT) ELEVATION OF ANY NEW OR

SUBSTANTIALLY IMPROVED BUILDING COVERED BY THIS PERMIT.

Plans and Specifications Approved this _____ day of ____________________, 2017.

___________________________________ ____________________________________

(Signature of Developer/Owner) (Authorizing Official)

cc: Water Resources Section

Iowa Department of Natural Resources

Wallace State Office Building

East 9th and Grand

Des Moines, IA 50319